## Slide 1
Water Treatment
Topics: Water softening methods: - Lime-soda, Zeolite and ion exchange processes and their applications. Specifications of water for domestic use (ICMR and WHO); Unit processes involved in water treatment for municipal supply - Sedimentation with coagulant- Sand Filtration - chlorination; Domestic water purification – Candle filtration- activated carbon filtration; Disinfection methods - Ultrafiltration, UV treatment, Ozonolysis, Reverse Osmosis; Electro dialysis.
Module-2

## Slide 2
Lime[Ca(OH)2] required for softening
[ Temp. Ca2+ + 2×Temp. Mg2+ + Perm. (Mg2+ + Fe2+ + Al3+)
+ CO2 + H+ (HCl or H2SO4) + HCO3-] x Volume of water(V)
74
100
All components in CaCO3 equivalent
V = volume of water
Final result in mg >>> kg
100 parts by mass of CaCO3 ≡ 74 parts of Ca(OH)2
1 part of CaCO3 ≡ 74/100 of Lime
Soda [Na2CO3] required for softening
[ Perm. (Ca2+ + Mg2+ + Fe2+ + Al3+) + CO2 + H+ (HCl or
H2SO4) - HCO3-] x Volume of water (V)
106
100
100 parts by mass of CaCO3 ≡ 106 parts of Ca(OH)2
1 part of CaCO3 ≡ 106/100 of Lime

## Slide 3
Lime Soda Process - Reactions of Lime and Soda
Ca(HCO3)2 + Ca(OH)2 → 2 CaCO3 ↓ + 2 H2O
Lime removes the temporary hardness:
Mg(HCO3)2 + 2 Ca(OH)2 → 2 CaCO3 ↓ + MgCO3 ↓ + 2 H2O
Soda and Lime removes the magnesium permanent hardness:
MgCl2 + Ca(OH)2 → CaCl2 + Mg(OH)2 ↓
CaCl2 + Na2CO3 → CaCO3 ↓ + 2 NaCl
MgSO4 + Ca(OH)2 → CaSO4 + Mg(OH)2 ↓
CaSO4 + Na2CO3 → CaCO3 ↓ + Na2SO4

## Slide 4
Soda removes all calcium permanent hardness:
CaCl2 + Na2CO3 → CaCO3 ↓ + 2 NaCl
CaSO4 + Na2CO3 → CaCO3 ↓ + Na2SO4
Reaction of CO2:
CO2 + Ca(OH)2 CaCO3 + H2O
Reaction of H+:
2 H+ + Ca(OH)2 Ca2+ + 2 H2O
Ca2+ + Na2CO3 CaCO3 + 2 Na+
Reaction of HCO3‒ (Example: NaHCO3)
2HCO3‒ + Ca(OH)2 → CaCO3 ↓+ CO32‒ + H2O

## Slide 5
Example
1. Calculate the amount of lime and soda required for softening 50,000 liters of hard water containing Ca(HCO3)2= 81 ppm, Mg(HCO3)2 = 73 ppm, CaCl2 = 222 ppm, MgSO4= 180 ppm, Na2SO4 = 15 ppm, NaCl = 165 ppm, and Fe2O3 = 25 ppm.

## Slide 6
Example
1. Calculate the amount of lime and soda required for softening 50,000 liters of hard water containing Ca(HCO3)2= 81 ppm, Mg(HCO3)2 = 73 ppm, CaCl2 = 222 ppm, MgSO4= 180 ppm, Na2SO4 = 15 ppm, NaCl = 165 ppm, and Fe2O3 = 25 ppm.
Sol: No hardness is caused by Na2SO4, NaCl, and Fe2O3 (insoluble solid), so they should not be included in the calculations.
Constituent | ppm | Multiplication factor (M.Wt. of CaCO3/ M.Wt. of Constituent) | CaCO3 equivalents
Ca(HCO3)2 | 81 | 100/162 | 81 x 100/162 = 50 ppm
Mg(HCO3)2 | 73 | 100/146 | 73 x 100/146 = 50 ppm
CaCl2 | 222 | 100/111 | 222 x 100/111 = 200 ppm
MgSO4 | 180 | 100/120 | 180 x 100/120= 150 ppm
Conversion to CaCO3 equivalents

## Slide 7
Lime required for softening 50,000 L of Water
Soda required for softening 50,000 L of Water

## Slide 8
Calculate the amount of lime and soda required to soften 50000 L of the water sample containing Mg(HCO3)2 = 15.6 mg/L; Ca(HCO3)2 = 34.4 mg/L; MgSO4 = 60 mg/L; CaCl2 = 25 mg/L; MgCl2 = 35 mg/L; SiO2 = 25 mg/L; NaCl = 20mg/L. [Ca = 40; Mg = 24; H = 1; C = 12; O = 16; Cl = 35.5, S = 32]
Calculate the amount of lime (88.3% pure) and soda (99.2% pure) for treatment of 24,000 liters of water, whose analysis is as follows: Ca(HCO3)2 = 18.5 ppm; Mg(HCO3)2 = 1.42 ppm; MgSO4 = 1.90 ppm; CaSO4 = 1.34 ppm; CaCl2 = 1.75 ppm. Also calculate the carbonate and non-carbonate hardness of the water sample.

## Slide 9
Calculate the amount of lime and soda required to soften 50000 L of the water sample containing Mg(HCO3)2 = 15.6 mg/L; Ca(HCO3)2 = 34.4 mg/L; MgSO4 = 60 mg/L; CaCl2 = 25 mg/L; MgCl2 = 35 mg/L; SiO2 = 25 mg/L; NaCl = 20mg/L. [Ca = 40; Mg = 24; H = 1; C = 12; O = 16; Cl = 35.5, S = 32]
Lime = 4.789 kg
Soda = 5.796 kg
Calculate the amount of lime (88.3% pure) and soda (99.2% pure) for treatment of 24,000 liters of water, whose analysis is as follows: Ca(HCO3)2 = 18.5 ppm; Mg(HCO3)2 = 1.42 ppm; MgSO4 = 1.90 ppm; CaSO4 = 1.34 ppm; CaCl2 = 1.75 ppm. Also calculate the carbonate and non-carbonate hardness of the water sample.
Lime = 0.3 kg
Soda = 0.106 kg
non-carbonate hardness = 12.39 ppm
carbonate hardness = 4.141

## Slide 10
A sample water on analysis has been found to contain the following impurities in ppm: Ca(HCO3)2 = 48.6; Mg(HCO3)2 = 29.2; MgCl2 = 3.8; CaCl2 = 33.3; CaSO4 = 54.4; NaCl = 659. Calculate the quantity of lime and soda required for softening one million liters of water {Atomic weight: Ca = 40; Mg = 24; H = 1; C = 12; O = 16; Cl = 35.5, S = 32}
Calculate the amount of lime (85%) and soda (90%) required for softening 50,000 litres of hard water containing following impurities (mg/L): CaSO4 = 40, MgCl2 = 46, Mg(HCO3)2 = 82 , Ca(HCO3)2 = 35, KCl = 10

## Slide 11
Explain with chemical equations and calculate the amount of lime and soda needed for softening 1,00,000 liters of water containing the following: HCl = 7.3 mg/L; Al2(SO4)3 = 34.2 mg/L; MgCl2 = 9.5 mg/L; NaCl = 29.25 mg/L. Purity of Lime is 90% and purity of soda is 98%. 10% of Lime and Soda are to be used in excess in order to complete the reaction quickly.
Lime = 4.522 kg
Soda = 4.949 kg
6. Calculate the amount of lime and soda required for the treatment of 10,000l of water containing the following salts dissolved per litre. CaCO3=50 mg, CaCl2=11.1 mg, MgSO4=12 mg, NaHCO3=7.25 mg, silica=10 mg.

## Slide 12
7. Calculate the amount of lime and soda required for the treatment of 10,000l of water containing the following salts dissolved per litre. CaCO3=60 mg, CaCl2=11.1 mg, MgSO4=12 mg, NaHCO3=7.25 mg, NaHCO3 = 183.